###### DVR

4-Channel Digital Video Recorder

###### Manual

CONTENT

1. FEATURE	3

2. SPECIFICATIONS	4

3. INSTALLATION	5

4. FRONT PANEL	6

5. OPERATING MANUAL (MAIN MENU)	8

5.1 SYSTEM SETUP	8

5.1.1 PASSWORD SETUP	9

5.1.2 TIME SETUP	9

5.1.3 PTZ BAUDRATE SETUP	10

5.2 CAMERA SETUP	10

5.3 RECORD SETUP	11

5.4 PROGRAMMED RECORD	12

5.5 HARD DRIVE SETUP	12

5.6 SYSTEM RESTORE	13

6. VIEW CONTROL	13

7. PLAYBACK CONTROL	13

8. RECORD CONTROL	14

9. NTSC / PAL SYSTEM SETUP	15

10. PTZ OPERATION GUIDELINE ON THE FRONTPANEL	15

11.4CH RECORDING HOURS ON 80GB HARD DRIVE	16

12. DVR VIEWER USER GUIDE REVISION V2.3EN	16

12.1HARDWARE INSTALLATION	17

12.2 SOFTWARE INSTALLATION	17

12.3 EXECUTION	17

12.4 VIA THE ATTACHED USB CABLE TO PC	17

12.5 DVR VIEWER	18

12.5.1 VALID STREAM R REGION INDICATION	18

12.5.2 DIRECT ACCESS	19

12.5.3 EVENTS LIST BUTTON	19

12.5.4 OPTIONS BUTTON	19

12.5.5 STATUS BUTTON	19

12.5.6 RESET BUTTON	20

12.5.7 PLAY CONTROL	20

12.5.8 CHANNELS SELECTION	20

12.5.9 HDD SELECTION	20

12.5.10 CAPTURING BUTTON	20

12.5.11 MYS FILE PLAYER	21

1. FEATURE

1、Real Stand-alone Model

2、30 Frames Real Time Display Renew Rate.

3、Display With Real-time Recording.

4、Quad & Single Record Mode Optional

5、 NTSC/PAL System Optional.

6、 Improved MJPEG. Compression Format

7、 Support Hand, Mobile, Scheduled Record Mode

8、 Mobile Auto Alarm Record(Time Settable)

9、 As Per Date、Time, Quick Search Play Function.

10、Power recover auto restore record mode

11、Link to PC Through USB , and Backup DVR Data.

12、In Sets Motion Detect Function.

13、Infrared Remote Control and Panel Control.

14、Support PTZ Control.

15、Audio Function( Optional)

2. SPECIFICATIONS

| Operation system | Embedded RTOS |
| --- | --- |
| Video Input | NTSC/PAL |
| Video Input Channel | 4CH Composite |
| Video Output Channel | 2CH Composite (VCR OUT / MONITOR OUT) |
| Display Frame | NTSC | 120 fps (4x30 fps) |
|  | PAL | 100 fps (4x25 fps) |
| Recording Frame Rate(QUAD) | NTSC | Max 30fps |
|  | PAL | Max 25fps |
| Recording Frame Rate(EACH) | NTSC | Max. 7.5fps(30 fps/4) |
|  | PAL | Max. 6.25fps(25 fps/4) |
| Recording Mode | Continuous/motion/ Programmed |
| Resolution | Display | NTSC | 720x480 |
|  |  | PAL | 720x576 |
|  | Recording | NTSC | 640x224 |
|  |  | PAL | 640x272 |
| Compression Format | Advanced MJPEG | Low | 12KBytes/Frame |
|  |  | Normal | 15KBytes/Frame |
|  |  | High | 20KBytes/Frame |
| HDD | 250G/250G x 2 (with Audio) |
| Search Mode | Time / Date / Event |
| Full Screen | YES |
| Motion Detect | YES |
| Buzzer Output | YES |
| Brightness Adjust | YES |
| Contrast Adjust | YES |
| USB Output | YES |
| System a monitor | Power recover auto restore record mode |
| Power Supply | DC 12V / 4A(AC110V-240V 50/60HZ) |
| Dimension | 33.2cm x 26.8cm x 4.7cm (W x D x H) |
| Weight | 1.56KG |

3. INSTALLATION

Rear panel

(10)

(11)

(1) RS-485;

(2) HDD BAY;

(3) Main Output:Power DC 12V;

(4) Video Input1;

(5) Video Input2:.

(6) Video Input3:

(7) Video Input4;

(8) Audio Output;

(9)Audio Input;

(10)USB Input

(11)Power Input

4. FRONT PANEL AND REMOTE CONTROL

(1)  REC LED

(2)  POWER LED

(3)  REMOTE CONTROL RECEIVE

(4)  RECORD KEY

(5)  STOP RECORD/ ENTER PTZ OPERATION

(6)  PAUSE

(7)  ENTER /EXIT PTZ OPERATION MENU

(8)  SET/PTZ CAMERA

(9)  FREE

(10) DISPLAY WITH RECORD

(11) ENLARGER/FAST BACKWORD/+

(12) CH4 FULL SCREEN/PTZ LEFT /-

(13) UP/PTZ ZOOM IN

(14) DOWN/PTZ ZOOM OUT

(15) PICTURE2/PTZ LEFT

(16) QUAD PICTURE

(17) PICTURE3/ PTZ DOWN

(18) PICTURE1/PTZ UP

(19)PICTURE4/PTZ RIGHT

5. OPERATING MANUAL (MAIN MENU)

Press  to select items, useto enter,Press to exit.

5.1 SYSTEM SETUP

Press  to select items, useto enter. Press to exit and save data.

(1) Buzzer Alarm Time Setup: 1-30 s

(2) VLoss Alarm：ON/OFF.

(3) Motion Alarm：ON-OFF (4 Types),the front is Alarm; and the behind is jumping alarm picture.

(4)BAUDRATE: 2400、4800、9600、38400、57600、115200(6 Types).

Note:some function are subject to the mode.

5.1.1 PASSWORD SETUP

Select this item to change password:

(1) When the new password is accepted, the board will flash the following screen message: “PASSWORD CHANGING”.

(2) If the password was not accepted, you will receive a message: INCORRECT”.

※Use the view control button on the front panel to input the number.

※Factory default password:111111.

5.1.2 TIME SETUP

Select this item to set up current time.

Time format: yyyy/mm/dd

Press  to select items, useto enter. Press to exit and save data.

Show Time setup:

UP 1: Displayed on up-right corner of the screen, date & time listed in a row.

UP 2: Displayed on up-right corner of the screen, date & time listed in two rows.

DOWN1: Displayed on down-right corner of the screen, date & time listed in a row.

DOWN2: Displayed on down-right corner of the screen, date & time listed in two rows.

5.1.3 PTZ BAUDRATE SETUP

Press  to select items, useto enter. Press to exit and save data.

Baudrate setup:

Acceptable Baudrate: 2400、4800、9600、38400、57600、115200(6 Types).

5.2 CAMERA SETUP

Press  to select items, useto enter. Press to exit and save data.

(1)Camera select (default value CH1)

(2)Record set up: yes or no record.

(3)Brightness / Contrast Set UpRange :00—11, default value is 5.

(4)Motion set up: motion detector, ON/OFF.

(5)Sensitivity set up: sensitivity from 0—15 grades are selectable.

5.3 RECORD SETUP

Press  to select items, useto enter. Press to exit and save data.

(1) Record Setup: EACH MODE (frame recording)

,                            QUAD MODE (quad recording)

(2) Video Quality: video quality selection: High, Normal, Low.

(3) Record Frame Rate:

A.QUAD MODE frame rate alternatives as follows:

→25、12、8、6、4、3、2、1 fps.

In this mode 、、、are selectable to go on PTZ operation.

B.Each Mode frame rate alternatives as follows:

→Maximum : 6.25 fps each camera totally: 25 fps = 6.25 x 4 CH

(4) Motion Record Frame Rate is different from Normal Rate. Setting Alarm Record Frame Rate high to get more important information from your record.

(5) Motion Record Time: maximum 60 seconds sensor record time.

※(4)(5) Record Schedule only valid in “ M “ selection Time.

※Above settings are PAL Mode settings, Setting NTSC Mode in a similar way.

5.4 PROGRAMMED RECORD

Press  to select items, useto enter. Press to exit and save data.

(1)Use to change record mode.

(2)Range: 0-24 hours

(3)Set “T” for continuous recording.

(4)Set “M” for sensor recording. Please refer to 5-3 ALARM setup.

(5)Set up “-” to exit the record.

★If you want to enable Motion Recording, Please follow the setup procedure a and b:

a. Select “MOTION SETUP: ON” in the menu option “CAMERA SETUP”.

b. Set “PROGRAMMED RECORD” --- “M” in the menu option “RECORD SCHEDULE”

5.5 HARD DRIVE SETUP

Press  to select items, useto enter. Press to exit and save data.

(1)Overwrite Enabled

YES: Overwrite. 4hours as a unit.

NO: Stop Recording.

(2)Master HDD Status

Indicates the use of the master HDD including volume &used percentage

(3)Master Format

Select this item to format HDD, screen show: PASSWORD INPUT

(6) ------ 6 digits. If password correct, the screen shows: “password       correct “, Otherwise, it shows: “password incorrect. “

※  Factory default password:111111.

※ HDD must be formatted before installation, replacement & re-installation.

5.6 SYSTEM RESTORE

Restore the default settings.

6. VIEW CONTROL

(1)Can use the following view control to monitor images from cameras.

Camera #1 (CH1), return to Quad Mode by press again.

Camera #2 (CH2), return to Quad Mode by press again.

Camera #3 (CH3), return to Quad Mode by press again.

Camera #4 (CH4), return to Quad Mode by press again.

(2)Prior to view control, HDD must be formatted. Either “EACH MODE” or “QUAD MODE” should be selected. (Refer to 5-3)

(3)In mode of “QUAD MODE”, view control is only for quad display not available for CH1, CH2, CH3, and CH4.

7. PLAYBACK CONTROL

(1)Press  , and the system shows the recorded period.

(2)Each period is as four hour

Press  to select EVENT or DATE/TIME, pressto exit.

(1)EVENT:

Press choose one period, then press to play.

(2)DATE / TIME:

The signal”>” goes up to the “HARD DRIVER: MASTER”. Press to select items. Use select to change data, and then press to play.

(3)PLAYBACK:

*Press to speed forward. Continue to press and show x2、x4、x8 multiple playing.

*Press to show x2 multiple back motion.

*Press to pause.

*Pressto stop.

8. RECORD CONTROL

(1)Press "" key to start recording. Icon “" indicates recording.

(2) During recording, the mark” *” appears in status of overwriting.

9. NTSC / PAL SYSTEM SETUP

J1 Jumper Setting as follow:

10.PTZ OPERATION GUIDELINE ON THE FRONTPANEL

※The default addresses of CH1,CH2,CH3,CH4 dome are 01、02、03、04. If addresses are incorrect, you can not control those.

You can press  into PTZ Operation Mode, when DVR run in monitor mode or REC mode. If you press again, it can change camera. If you press 4 times, it will exit PTZ Operation Mode.

11. 4CH RECORDING HOURS ON 80GB HARD DRIVE

*Thereinafter a rough estimate a table for reference only, recording data quantity can follow an image a variation a rate somewhat different.

| Recording Results in NTSC Format | 30fps | 15fps | 7fps | 1fps |
| --- | --- | --- | --- | --- |
| Video Signal | Display Format | Video Quality |  |  |  |  |
| NTSC | QUAD MODE | High | 36Hours | 72Hours | 144Hours | 1080Hours |
|  |  | Normal | 48Hours | 96Hours | 192Hours | 1440Hours |
|  |  | Basic | 58Hours | 116Hours | 232Hours | 1740Hours |
|  | EACH MODE | High | 64Hours | 128Hours | 256Hours | 1920Hours |
|  |  | Normal | 90Hours | 180Hours | 360Hours | 2700Hours |
|  |  | Basic | 112Hours | 224Hours | 448Hours | 3360Hours |
| Recording Results in PAL Format | 25fps | 12fps | 6fps | 1fps |
| Video Signal | Display Format | Video Quality |  |  |  |  |
| PAL | QUAD MODE | High | 38Hours | 76Hours | 152Hours | 950Hours |
|  |  | Normal | 48Hours | 96Hours | 192Hours | 1200Hours |
|  |  | Basic | 60Hours | 120Hours | 240Hours | 1500Hours |
|  | EACH MODE | High | 62Hours | 124Hours | 248Hours | 1550Hours |
|  |  | Normal | 90Hours | 180Hours | 360Hours | 2250Hours |
|  |  | Basic | 118Hours | 236Hours | 472Hours | 2950Hours |

12. DVR VIEWER USER GUIDE REVISION V2.3EN

Introduction

This document is the Operation Manual for DVR Viewer. The application will show you stream image stored in the HDD which was previously formatted and recorded by the DVR.

If any DVR HDD is connected to your PC, the application will automatically detect the HDD and show the recorded stream. You can also save the current screen to a BMP file, and save the current stream to a MYS stream file or an AVI file.

※We suggest to backup the video stream in MYS format for the fast speed.

The application consists of two functional modules:

| DVR HDD PC Viewer | Shows stream stored in the HDD directly. |
| --- | --- |
| MYS File Player | Plays captured stream MYS file. |

Requirement:

| OS | 2000 SP4 / XP SP2 or later |
| --- | --- |
| DirectX | DirectX 7.0 or later |

Recommendation:

| ◆ CPU | 1.0 GHz or Higher |
| --- | --- |
| ◆ RAM | 256 MB or Greater |

12.1 HARDWARE INSTALLATION

◆As stated above, the application shows stream which is stored in DVR HDD.

◆Before installing and executing the application, make sure that you connected DVR

◆HDD to the IDE cable of your PC directly, or via USB HDD adaptor

12.2 SOFTWARE INSTALLATION

◆Make sure that the OS of your PC is Windows 2000 SP4 or later [XP SP2 or 2003]. Otherwise, the application will not operate properly.

◆Double click on the DVR_Setup.exe to install the program.

12.3 EXECUTION

◆Just double click the shortcut of the execution file.

◆The application first detects physical HDDs installed at your PC and search for DVR HDD among them. This process may take up to 1 minute.

12.4 VIA THE ATTACHED USB CABLE TO PC

a. Connect USB cable both ends to the USB port of the DVR and your PC.

b. Supply 12VDC power to the DVR.

c. Wait until the message of USB detected pops up on the VGA monitor.

d. Run the PC Viewer software accordingly.

e. Wait until the very first image comes up to the PC Viewer.

f. Click “Play” icon on the control panel of the PC Viewer to start viewing the video files.

12.5 DVR VIEWER

User Interface:

Functions

12.5.1 VALID STREAM R REGION INDICATION

Once a DVR HDD is selected, the application detects valid stream region where valid video stream resides. You can drag this to access the whole streams of the DVR HDD.

12.5.2 DIRECT ACCESS

If the stream stored in a DVR HDD is quite long, you may have difficulty to find the exact scene you want to see. When you find a scene you would like to show your friend or report to police officers later, please remember the number in the Direct Access Input edit box, so that you can go there directly by entering the number in the edit box and pressing “GO” button besides it.

12.5.3 EVENTS LIST BUTTON

You can access the latest 64 events and go to the event directly by this button.

12.5.4 OPTIONS BUTTON

You can change application settings such as MYS file save directory, or default video mode (NTSC/PAL). To change setting, press Options button

12.5.5 STATUS BUTTON

Show the status on the screen.

12.5.6 RESET BUTTON

Reset the program.

12.5.7 PLAY CONTROL

Once a DVR HDD is selected, the application automatically displays first screen recorded at the very beginning of it. Then, you can see stream at anywhere within the valid stream reason.

12.5.8 CHANNELS SELECTION

The default screen display channel setting is ALL CHANNEL, which shows all four channel (if the stream has 4 channel streams) at the same time. If you want to see a channel only or enlarge one channel, press any channel button you want.

12.5.9 HDD SELECTION

Once the application detects one or more DVR HDDs, it automatically selects the first DVR HDD. You can select any DVR HDD [the DVR HDDs are marked as "VY HDD ". However, you cannot select the normal HDD, which may be Windows-formatted one.

12.5.10 CAPTURING BUTTON

Screen Capturing

If you want to capture, or backup, current screen, press Capture Current Screen button. Then it will capture the current screen and saves it as BMP file.

Stream Capturing Button

If you wan to capture, or backup, current stream, press Capture Current Stream button. Then it will record the stream you want. It will create .MYS file, whose format is Vineyard Technologies’ proprietary stream file format. You can play the recorded file using MYS file player.

Stream Capturing Button

If you wan to capture, or backup, current stream, press Capture Current Stream button. Then it will record the stream you want. It will create .AVI file. You can play the recorded file using any player which support AVI file.

12.5.11 MYS FILE PIALER

You can play the recorded MYS file using MYS file player.

# Text boxes

MAIN MENU

SYSTEM SETUP

CAMERA SETUP

RECORD SETUP

RECORD SCHEDULE

HARD DRIVE SETUP

SYSTEM RESTORE

(): SELECT (): SET (): EXIT

SYSTEM SETUP

BUZZER ALARM TIME   : 03 S

VLOSS   ALARM       : ON

MOTION  ALARM      : OFF-OFF

PASSWORD SETUP

TIME SETUP

BAUDRATE             2400

(): SELECT (): SET (): EXIT

OLD PASSWORD: ______

NEW PASSWORD: ______

CONFIRM: _ _____

TIM`E SET

2004/12/17 18:00:30

SHOW: UP 1

(): SELECT (): SET (): EXIT

CAMERA SETUP

CAMERA            : CH1

RECORD SETUP      : ON

BRI SETUP           : 05

CON SETUP          : 05

MOTION SETUP      : OFF

SENSITIVITY SETUP  :05

(): SELECT (): SET (): EXIT

RECORD SET

RECORD SETUP           EACH MODE

VIDEO QUALITY           HIGH

RECORD FRAME NO.     25FPS

MOTION REC FRAMERATE 25FPS

MOTION RECORD TIME    10S

(): SELECT (): SET (): EXIT

PROGRAMMED RECORD

(): SELECT (): SET (): EXIT

HARD DRIVE SETUP

OVERWRITE ENABLED  (YES)

MASTER HDD SIZE     80000MB

MASTER HDD USED    10MB 0 %

MASTER HDD FORMAT

SLAVE HDD SIZE        N/A

SLAVE HDD USED       N/A

SLAVE HDD FORMAT

(): SELECT (): SET (): EXIT

SEARCH TIME

HARD DRIVER: MASTER

06/04/01 02:47:56 - 06/04/01 02:47:56

01 TIME 2006/12/10 02:47:50

02 TIME 2006/12/10 02:47:50

03 TIME 2006/12/10 02:47:50

():SELECT ():SET （）:PLAY

(): EXIT () SELECT EVENT/TIME

(16)

(6)

(7)

(8)

(9)

(10)

(15)

(7)

SYSTEM SETUP

BUZZER ALARM TIME   : 03 S

VLOSS   ALARM       : ON

MOTION  ALARM      : OFF-OFF

PASSWORD SETUP

TIME SETUP

BAUDRATE             2400

(): SELECT (): SET (): EXIT

: Into PTZ Mode and CAMERA+

: Up

: Left

: Down

: Right

- : Enlarge

- : Minufy

- : Stop

- :Automatic detect

: Setup speed: the range is1-7。