# QUAD PROCESSOR 

Directory

- System feature

- Description of function the front panel keys

- The interface of back panel

- Menu

(V)The Remote Controller Operation

(VI)Technology specification

NB some of the features herein describe the 8 camera version and are not available on this 4 camera version.

- SYSTEM FEATURES

- Connect the 1-4 line video Signal of camera and than brightness,

# Saturation, contrast color ,HUE and sharpness.

- High definition

# NTSC mode :720X480,60HZ PAL mode;720X576,50HZ

- multiple display mode

eight Pictures, four pictures, two pictures, single pictures, PIP(picture eight Picture)automatic inverting mode

- High performance picture frozen function

# Glitter picture catch

- High performance picture amplifying function

# The area to be zooming in can be selected.

- The various fonts folded information

# The title of camera,real time display and warning date/video/moving detecting information

- The four pictures and single picture mode recycle

- There are multiple mode:

# Warning input, video loss detection, moving detection can keep over 60 reports, the built in buzzer

- THE FRONT PANEL INSTRUCTION

| From left rightwards | MENU A/B | AUTO FRE | ZOOM MODE | VCR ENT | 1/5 U | 2/6 D | 3/7 L | 4/8 R |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Grow to perss | Menu | Auto | Enlarge | Retum to put | 1/5 apperrance | 2/6 apperrance | 3/7 Appearance | 4/8 appearance |
| Short perss | A/B Cut over | Grasp to clap | Show the mode | Confirm | Last key | Next key | Left key | Right key |

The key definition:the short press should not linger than a seconds and the long press should be longer than 1 seconds

  - MENU key. Press it for a long time to enter main menu, press the short press key to enter page A or gage B

  - AUTO key: press it for a long time to enter main menu ,press the short press is picture frozen

  - ZOOM :press it for a a long time to zoom in and press it short timely for the first time is eight pictures and the second time is the picture in two picture.

  - VCR key press it for a long time and go to loop and press it  short time to enter menu confirm key .

  - “1/5”key :It is the first and fifth passage of the camera. there are the up and left moving functions

  - “2/6”key :it is the second and sixth passage of the camera .There are the down and right moving functions

  - “3/7”key :it is the third and seventh passage of the camera .There are left and decease function

  - “4/8”key:it is the forth passage and the eighth passage of the camera. There are right increase function

III：THE BACK PANEL INSTRUCTION – note this image is of the 8 camera version – not the 4 camera version being sold.

IV、MEVU

The steps: Under any mode in the sport ,press the MENU for a long time and you can enter to the main,menu.

1.Menu setting and modifying ways: press MENU and enter the main menu and press“▽△”to move the cursor to the selected items. Press ENTTER key to enter confirm and press“▽△”to move horizontally. Press “      ”key is increase and decrease value.

4.1 SYSTEM SETUP

In the main mode use“▽△”and select “SYSTEM” and press“ENTER key to enter setting item

- DATE is date ,yesr,,month,day.Setting  TIME is time,hour,minutes and second setting

  - SYSTEM is the patten setting of NTSC and PAL

    - KEY LOCK is lock of the front panel keys

      - FACTORY RESET:it is the factories

Note:set the NO to YES and press ENTER

Confirm and select YES and press ENTER key to confirm and reset

4.2 DISPLAY SETUP

In the main menu mode use“▽△”key and select PLAY with cursor and press ENTER key to inter the setting item

- TITLE is the title switch of the camera

- ADTE the date switch

- TIME is the time switch

- SCREEN POSTION are the setting of coordinate division

- Black is the black color and GRAY1 is and GRAY2 is offwhite.

OFF is division switch.

4.3AUTO SEQUENCE

Under the main menu“▽△”key to select AUTO and press ENTER key to enter the setting item

- PADEA means the channel shift time of QUADA and CAMI-CAM4 pictures picture

Use the “▽△”key to select CAMERA SETUP and then press“ENTER” to enter setting item

“TITLE”means the title setting mode .Press“▽△”and the font box will appear.You can change the title according to the word ing the box

BRIGHTNESS CONTRAST SATURTION HUE SHARPNESS are adjustable brightness, contrast ,hue and sharpness.

MIRRORING is the photo setting mode .When the setting is selected to be ON,the input signal will be displayed in with contrast displayed in with contrast direction ,The default setting is OFF. Press MENU to exit

4.5 MOTION SETUP

In the mail menu mode ,use “▽△”to select MOTION SETUP and press ENTER to enter the setting item

- “DETECTION TIME”is the switch setting of the detecting time and it is available when the setting is in the state of “ALWAYSON”

- SENSITIVTY means the sensitivity of detection

- MASKING AREA means the area coordinate of detecting time

4.6 EVENT SETUP

In the main menu, use the “▽△”and select EVENT SETUP and then press enter key to enter the setting item.

- ALARM,LOSS MOTION extended warning ,video loss,and moving detection open/close setting

- BUZZER HOLD TIME means the extend time of the recorded events

- REPORT HOLD TIME means the extended time of the recorded events

- ALARM PLARITY is the high and low voltage setting of the buzzer

4.7 EVENTREPORT

In the main menu,use“▽△”key and select EVENT REPORT and press EVENT REPORT and press ENTER to go to the setting item.

V.Remote controller operation

The system provides two remote controllers,RS-232interface and infrared transmitter .The following control panel is used for both remote controllers. The operating method for both controllers is described in this section.The detail RS-232C protocol will be explained the RS-232C Interface section.

Setup Menu Operation

The system provides a built –in GUI setup screen. For each menu ,the key function is described in the lower region to help operation. The following figure shows the structure of GUI menu.

This system accepts up to 8 alarm inputs and provides alarm output with COMMON signal.

A1-A4:Alarm inputs    GND: Ground from the sensors

N.O:NORMAL Open alarm output  COM:COMMON alarm output

VI:TECHNIC SPICIFICATION

| VIDEO STANDARD | PAL：50fields/sec NTSC：60 fields/sec |
| --- | --- |
| Definition | PAL： 720X576 NTSC：720X480 |
| Video input | 1．0VP-P75 ohm input |
| Tape input | 1．0VP-P75 ohm input |
| Tape out | 1．0VP-P75 ohm output |
| Alarm mode | Video lost warning ,touch and start mode, moving detection warning |
| Video input mode | Full screen, electronic amplifying ,eight pictures, four pictures, PIP and automatic |
| Working voltage | DC12V/1A |
| Environmental temperature | -300C-600C |

# Text boxes

SYSTEM

SETUP

DISPLAY

SETUP

AUTO

SEQUENCE

CAMERA

SETUP

MOTION

SETUP

EVENT

SETUP

EVENT

REPORT

DATE：YY-MM-DD

04-01-01

TIME：HH：MM：SS

12：00：00

SYSTEM FORMAT：PAL

SYSTEM ID NUMBER：01

KEY    LOCK：OFF

FACTORY     RESET：ON

DISPLAY  ON  SCREEN

(TITLE  (DATE  (TIME

SCREEN    POSITION   X： 0

Y： 0

BORDER   COLOR

( BLACK

(GRAY1

(GRAY2

( WHITE

(OFF

PAGE A QUAD：  01    SEC

CAMERA1：  01	   SEC

CAMERA2：  01	   SEC

CAMERA3：  01	   SEC

CAMERA4：  01	   SEC

RAGEB QUAD：  01	   SEC

CAMERA1：  01     SEC

CAMERA2：  01     SEC

CAMERA3：  01     SEC

CAMERA4：  01     SEC

CAMERA：1

TITLE：      CAMERAO1

BRIGHTNESS：   O

CONTRAST ：    O

SATURATION：   O

HUE        ：   O

SHARPNESS：   O

MIRRORING：    OFF

（Picture）

CAMERA：1

DETECTION      TIME

ALWAYS         ON

ON：            11：00

OFF：           12：00

SENSITIVTY：   O

VELOCITY       O

MASKING       AREA

X，Y：（00，00）

Picture

BUZZER/REPORT     CONTROL

| CHANNEL | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ALARM | ( | ( | ( | ( | ( | ( | ( | ( |
| LOSS | ( | ( | ( | ( | ( | ( | ( | ( |
| MOTION | ( | ( | ( | ( | ( | ( | ( | ( |

BUZZET   HOLD  TIME  ： 05  SEC

REPORT   HOLD  TIME  ： 30  SEC

ALARM   POLARITY     ： LOW

1/6   PAGE

| NO | DD-MM-YY | HH：MM：SS | CH | EVENT |
| --- | --- | --- | --- | --- |
| 01 |  |  |  |  |
| 10 |  |  |  |  |

LIST       CLEAR：NO

SYSTEM SETUP

FACTORY RESET

DISPLAY SETUP

AUTO SEQUENCE

CAMERA  SETUP

SETUP MENU

MOTION SETUP

EVENT LIST

EVENT LIST CLEAR

GND

N．O

TXD

A5

RXD

A8

A7

COM

A6

GND

N．O

TXD

A1

RXD

A4

A3

COM

A2